## Slide 1
      CHE 352A PROJECT
160651 SHIVALI AGRAWAL

## Slide 2: Problem Statement
Objective: To simulate a multicomponent distillation column using Naphtali and Sandholm Newton-Raphson algorithm.
Given: Feed composition, Distillation column details.
Thermodynamic Models: WILSON model for activity coefficients, Redlich-Kwong for vapour phase fugacity coefficients and vapour enthalpy departure function.
Convergence method: Newton-Raphson
To Find: Block temperature profile, vapour and liquid compositions at each stage.

## Slide 3: Naphtali Sandholm Algorithm for multicomponent distillation
NS equations with Murphree plate efficiency-
Material Balance (M) :
  Mij = ( 1 + Si) * Vij + (1 + si) * Lij - Vi+ 1,j - Li-1,j - fij
Equilibrium Relations (E) :
  Qij = (ni * Kij * Vi * Lij / Li) - Vij + ((1 - ni) * Vi+1,j * Vi / Vi+1)
Enthalpy Balance (H):
  Ei = (1 + Si) * Hi + (1 + si) * hi - Hi+1- hi-1- hji
Murphree Plate Efficiency Equation : ni * Kij * xij - yij + (1 - ni) * yi+1,j = 0
.

## Slide 4: Degree of Freedom Analysis
Variables → (11+3c)N-1:
  Number of stages (N) : 1
  Temperature and Pressures of each stage: 2N
  Temperature and Pressure of each Feed: 2N
  Q for each stage: N
  F, W, U, V, L for each stage: 5N
  Tray efficiency for stage inside the column: N-2
  Mole fractions of components (Vapour, Liquid, Feed) on each stage: 3cN
Equations → (2c+3)N:
  Material balance of each component on each plate: cN
  Equilibrium relation for each component on each plate : cN
  Summation equations: 2N
  Enthalpy balance on each plate: N
Degrees of Freedom: Variables - Equations= (c+8)N-1
Specified in problem → (c+8)N-1:
  Number of stages (N) : 1
  Feed rates and Feed composition on each stage: N+cN
  Pressures of Feeds and Stages: N+N
  Temperature of Feeds: N
  Q each stages inside the column (which are all zero): N-2
  Reflux ratio and Bottom flow rate: 2
  Tray efficiency for stages inside the column: N-2
  Vapour and Liquid side streams all zero: 2N
Since we have specified DoF variables, our problem is properly defined and we can proceed with solving.

## Slide 5: APPROACH
1) Guess the initial matrix X using Rachford-rice algorithm for vapour and liquid compositions and linearly interpolate the temperature profile.
2) Calculating the matrix F by obtaining the enthalpy, material, equilibrium equations (MEH equations) for every stage.
3) Making of the derivative matrix dF/dx by calculating A, B and C matrices.
4) Applying Newton-Raphson algorithm to update the value of X.
5) Iterate till convergence.

## Slide 6: Initialisation of the X matrix
Guess for Temperature: Linear interpolation between the maximum to minimum boiling point from lowest to highest stage.
Guess for liquid and vapour fractions: Using Rachford-Rice algorithm considering the entire column as a single flash (with T_flash=T_feed-plate).
For the above step, the liquid and vapour mixtures were assumed to be ideal and therefore k=Psat(T)/P.

## Slide 7: MEH equations for the F matrix
Material Balance equations for each component at every stage (given by the function: ‘Material.m’):
Equilibrium equations for each component at every stage (given by the function: ‘Eij_RK.m’)
Fugacity coefficients are calculated using Redlich Kwong equation of state using the following eqn.
a and b are calculated by mixing rules

## Slide 8
Enthalpy Equation for each stage: (given by the function ‘hj.m’)
Where the enthalpy departure functions are calculated as:
where,
Enthalpy of vapour is calculated as:
Enthalpy of liquid is calculated as:
Here, T=330K is taken as the reference temperature
These 2 equations are used for the enthalpy balance for the first and the last stage respectively because Q values were not given
, L - B

## Slide 9: Making the df/dx matrix
The df/dx matrix (209 X 209) is calculated by computing the matrices Aj, Bj, Cj → which are Jacobian of the Fj with respect to Xj-1,Xj and Xj+1 respectively.
The derivatives of the Hj, Mij and Eij equations w.r.t vij, Tj and lij were required for the computation of the A, B, C matrices. For this central difference method was used for numerical differentiation.

## Slide 11: Convergence
Used Newton Raphson algorithm for updating the value of X matrix.
The convergence is achieved when tau becomes less than epsilon.

## Slide 12: ASPEN Results
Block Temperature Profile:

## Slide 13
Liquid Composition Profile
Vapour Composition Profile

## Slide 14: MATLAB Results- Block Temperature Profile

## Slide 15: Concentration Profiles (MATLAB)

## Slide 16: References
[1] Naphtali, L. M. & Sandholm, D. P. Multicomponent Separation Calculations. (1971).
[2] Seader, Junior D., Ernest J. Henley, and D. Keith Roper. "Separation process principles." (1998).
[3] Koretsky, Milo D. Engineering and chemical thermodynamics. Vol. 2. New York: Wiley, 2004.
[4] Gmehling and Onken, Vapor-Liquid Equilibrium Data Collection, DECHEMA Chemistry Data ser., vol. 1 (parts 1–10), Frankfurt, 1977.
[5] Perry, John H. "Chemical engineers' handbook." (1950): 533.
[6] R. L. Rowley, W. V. Wilding, J. L. Oscar- son, Y. Yang, N. A. Zundel, T. E. Daubert, R. P. Danner, DIPPR® Data Compilation of Pure Chemical Properties, Design Institute for Physical Properties, AIChE, New York (2007).
[7] https://in.mathworks.com/help/matlab/
[8] Aspen Plus 8.8 (2001) by Aspen Technology.